## Slide 1
Relevant standards and guidelines:
Assessment documents
For the components specifications and assembly drawings shall be submitted
Assembly and sectional drawings (associated parts lists and if applicable individual , part drawings, description explaining the functional principle of the blade pitching system.)
The calculations for the verification of the components of the blade pitching system shall be presented.
Evaluation of Pitch Teeth: Required Drawings for Pitch Gearbox Systems (Pitch Pinion, Pinion shaft, blade bearing teeth)
The analysis of: the pitch gearbox teeth, the blade bearing teeth, the blade bearing teeth, load capacity considering the fatigue loads, static strength against tooth breakage and pitting, Fatigue strength and static strength for the output shaft of the pitch gearbox and for the connecting elements of a pitch system
In the case of hydraulic actuator, dimensioned drawings with the maximum and minimum positions the positions in which the greatest loads act on the blade pitching mechanism.
fatigue strength analysis and static strength analysis for all loads.

## Slide 2
Relevant standards and guidelines:
Loads to be applied
The static and load-dependent bearing friction moments shall be taken into account.
Fatigue Analysis (Load Considerations)
Use Load Duration Distributions (LDD) or Load Spectra
Distinguish Between Operation With and Without Blade Pitching
Include Additional Inertial Loads from Rotor Rotation
Consider Dynamic Vibration-Exciting Loads
- Static Strength Analysis for Pitch Systems
Analyze With and Without Blade Pitching Operation
Use Design Loads from the Dimensioning Load Case
If Maximum Torque is Exceeded:
  Consider Torque from Pitch Motor Brakes or Hydraulic Pressure
  Use Maximum Torque Generated by the Pitch System for Analysis

## Slide 3
Relevant standards and guidelines:
Loads to be applied
Blade Bearing Teeth Stress Analysis
Teeth are Stressed on a Small Part of Their Circumference
Maximum Rotation Angle Between Start and Stop: ~90°
Load Cycles for Gear Calculation:
  Determine Appropriately
  Multiply by Factor Based on Sector of Teeth Used
- Rotary Drive Systems: Strength Analysis
Use Application Factor: KA = 1.0
Applies to Static and Fatigue Strength Analysis